OPERATING INSTRUCTIONS FOR 35mm BADGE MAKER:

# Text boxes

- Slide bottom die to the far left hand side and load with metal badge front, your cut out artwork and plastic mylar.

- Slide bottom die to the far right, ensure top and bottom dies are aligned, gently pull down handle until top die picks up the contents of the bottom die.

- Load right hand die with pinback (pin facing down).

- Slide bottom die to the left hand side until top and bottom dies align again, gently pull down the handle until top and bottom die compress together. (For extra efficiency, you can begin loading your components into the left hand die again to begin another badge).

- Slide bottom die to the right and there is your finished button badge. (And if you’ve loaded the next badge already go back to step 3 and repeat!)

- de bottom die to the far right, ensure top and bottom dies are aligned, gently pull down handle until top die picks up the contents of the bottom die.

- Load right hand die with pinback (pin facing down).

- Slide bottom die to the left hand side until top and bottom dies align again, gently pull down the handle until top and bottom die compress together. (For extra efficiency, you can begin loading your components into the left hand die again to begin another badge).

- Slide bottom die to the right and there is your finished button badge. (And if you’ve loaded the next badge already go back to step 3 and repeat!)