Floss Into Bags

The

Australian Way

Devised by Ronald N. Smart

23 July 1995

Smart Amusements Pty. Ltd.

Fax, phone or email us at

Fairy Floss Supply Company,

Unit 15D, 56 Keys Road, CHELTENHAM VIC. 3192.

Phone (03) 9555 6606   Fax (03) 9555 9909

1.	Making Floss into bags is best carried out in an air

conditioned room to regulate humidity, the enemy

of floss bagging.

Sugar is best stored in the making room to

dehumidify it. These instructions are designed for

a right hand person using 200mm x 300mm poly

drop 40UM bags with A SECOND PERSON

SEALING. Bags and machine should be at a level

you can comfortably cope with. Use disposable

rubber gloves on fingers to stop sticking.

The Method

Open bag by rubbing edges together with dusted

fingers. Lay bag on left hand wrist, palm up. Open

bag mouth while gripping the side of the bag with

fingers inside, thumb outside. With right hand,

pick up ring of floss.

Tuck first ring of floss into bag with fingers. Push

firmly down into bag bottom, firmly into corners.

THIS IS IMPORTANT, it shapes bag by keeping

mouth open for next ring of floss and ensures a

well filled, fat bag. Taking the part filled bag off the

wrist as shown in figure 3 is not recommended. This is

is only to show how to push it into the corners.Keep

bag resting on inside of wrist to make filling easier.

Figure 1.Bag laying palm side up in crook of

Arm. Bag is picked up ,flicked open and laid

In crook of arm.

Figure 3 Floss into corner of bag.

.

Figure 2 Stuffing first ring into bag.

Figure 4.

Tucking second

lifted ring of floss

into opened bag

resting on left hand

inner arm.

Pick up second ring, tuck into bag as before.

Continue with third ring handful of floss. This should be ample to fill bag.

Make sure third handful, which fills the bag, is tucked in well past the mouth of bag leaving

at least one inch clear for a clean electronic seal without floss strands trapped in sealing area.

Air can leak through strands left in opening before sealing and causes bag shrinkage.

Picture shows with greater clarity how the FIRST handful is pushed into the bottom corners

to fatten fill bag.

Floss makers all have favourite ways to bag, however  this method seems to be the most popular with

Australian show people.

Figure 5

Pushing second ring of

floss into bag after first

handful is tucked into

corners. This keeps

mouth and body of bag

wide open to feed third

handful to top of bag.

Tucking final

floss ring into

bag held on back

of hand. Bottom

gripped inside

bag with fingers.

The facts of life!!

Like everything in life, you only get what you pay for, be it Floss Machines, bags, colours

or whatever. Start with machines. Buy the best in Australia, an Aussie made ‘Smart Floss

machine.

Now to color. The cheapest is not the best, because it will be cut with sugar or salt. We

sell not the cheapest but the best for the price, and complies with World food regulations.

Our “FLAVA-COLOUR” is a combination of the best colour and fruity flavor in a castor base.

It is recommended for price, colour and quality. Flavacolor does not carbonise on your element.

Available in Rasberry Blue,Raspberry Pink,Mauve Bubblegum,Lime Green and

Banana Yellow.

Now To Bags.

“Cellophane” is great but is the most expensive single layer material available and not

great for keeping qualities. Needs both heat and pressure to seal satisfactorily.

Single layer cast poly-prop 24UM is the cheapest, clearest material but suitable only for

few days keeping quality . Thin 24UM walls are difficult to open, easy to split, and “El

Cheapo”.

Single layer cast poly-prop 4OUM . Good to work with, opens easily, if packed fat, tight

and stored correctly. Recommended as great middle of the road for strength, clarity and

keeping quality.

Multi layer laminates (two bags in one) are absolutely the best. They will keep weeks and

weeks if packed tight and sealed tight but are expensive. Most suitable for retail shops for

its long shelf life and ease to fill — very, very good bags. These are the stiff bags used for

packing quality confectionery or “Twisties” type product.

Sealers for Poly Prop Bags.

We recommend our electronic, hot wire impulse sealers bench and treadle models. Parts

and service available. We no longer sell old fashioned Cello Jaw Sealers.

R.N. Smart  1995